Wireless LANs I
Chapter 6
Panko and Panko
Business Data Networks and Security
Copyright © 2015 Pearson Education, Inc.

---
Introduction
Radio Signal Propagation
Radio Bands and Bandwidth
Spread Spectrum Transmission
802.11 WLAN Operation
802.11 Transmission Standards
Wireless Mesh Networking

---
6.1 802.11/Wi-Fi WLAN Technology
6.1 802.11/Wi-Fi WLAN Technology
Ethernet 802.3 LANs
  - Require standards at Layer 1 (physical) and Layer 2 (data link)
  - Therefore, use OSI standards
  - The 802.3 Working Group of the IEEE 802 Committee creates standards

---
6.1 802.11/Wi-Fi WLAN Technology
6.1 802.11/Wi-Fi WLAN Technology
Wireless LANs
  - Operate at Layers 1 and 2
  - OSI dominates at Layers 1 and 2
  - Therefore, they are OSI standards

---
6.1 802.11/Wi-Fi WLAN Technology
6.1 802.11/Wi-Fi WLAN Technology
802.11 Wireless LAN Technology
  - The dominant WLAN technology today
  - Standardized by the 802.11 Working Group of the IEEE 802 Committee

---
6.1 802.11/Wi-Fi WLAN Technology
6.1 802.11/Wi-Fi WLAN Technology
Wi-Fi Alliance
  - Industry association of 802.11 equipment manufacturers
    - 802.11 standards have many options
    - Wi-Fi Alliance selects subsets of standards as profiles
    - Does interoperability testing on these profiles
    - Only products that pass can display the Wi-Fi logo

---
6.1 802.11/Wi-Fi WLAN Technology
6.1 802.11/Wi-Fi WLAN Technology
Wi-Fi Alliance
  - However, sometimes develops new standards
    - Two have been security nightmares
    - WPA
    - WPS

---
6.2 Hybrid Switched/Wireless 802.11 Network
6.2 Hybrid Switched/Wireless 802.11 Network
The wireless access point connects the
wireless client to the wired Ethernet LAN.

---
6.2 Hybrid Switched/Wireless 802.11 Network
6.2 Hybrid Switched/Wireless 802.11 Network
The LAN connection is needed to give clients access to servers and Internet access routers on the wired LAN.

---
Introduction
Radio Signal Propagation
Radio Bands and Bandwidth
Spread Spectrum Transmission
802.11 WLAN Operation
802.11 Transmission Standards
Wireless Mesh Networking

---
6.3 Electromagnetic Wave
6.3 Electromagnetic Wave
Optical fiber transmission is measured in terms of wavelength.
Typical data LAN frequencies are 500 MHz to 10 GHz

---
6.4 Omnidirectional and Dish Antennas
6.4 Omnidirectional and Dish Antennas

---
6.4 Omnidirectional and Dish Antennas
6.4 Omnidirectional and Dish Antennas
Questions:
What type of antenna do mobile phones use?
Why?

---
6.5: Wireless Propagation Problems
6.5: Wireless Propagation Problems
2.
Electromagnetic
Interference (EMI) is unwanted power at the same frequency from other devices.
1.
Wireless transmission has many propagation problems.

---
6.5: Wireless Propagation Problems
6.5: Wireless Propagation Problems
Shadow zones are places the signal cannot penetrate because of obstacles in its path.
Shadow zones, also called dead spots,
grow worse as frequency increases.

---
6.5: Wireless Propagation Problems
6.5: Wireless Propagation Problems
The signal strength spreads out as the surface of a sphere.
This means that its strength falls as (1/r2), where r is the radius.
If you double the distance, you only get ¼ the signal strength

---
6.6: Inverse Square Law Attenuation
6.6: Inverse Square Law Attenuation
Radio signals spread out in a sphere.
  - S = signal power, r = range (distance) or radius
  - If the signal power at 10 meters is 9 milliwatts (mW), how strong is it at 30 meters?
S2 = S1 * (r1/r2)2
S2 = 9 mW * (10/30)2
S2 = 9 mW * (1/3)2
S2 = 9 mW * (1/9)
S2 = 1 mW

---
6.6: Inverse Square Law Attenuation
6.6: Inverse Square Law Attenuation
Your turn.
  - If the signal strength at 5 meters is 48 mW, how strong is it at 20 meters?

---
6.5: Wireless Propagation Problems
6.5: Wireless Propagation Problems
Signal is absorbed by the air and water.
Note that there are two types of attenuation: Inverse square law and absorptive attenuation.
Note that this is different than shadow zones.

---
6.5: Wireless Propagation Problems
6.5: Wireless Propagation Problems
Direct and reflected signals may interfere.
Most serious propagation problem at WLAN frequencies.

---
6.7: Multipath Interference
6.7: Multipath Interference
If the two waves are out of phase, they will negate each other, giving no signal.

---
6.5: Wireless Propagation Problems
6.5: Wireless Propagation Problems
Recap
Two forms of attenuation
Two grow worse at higher frequencies

---
Introduction
Radio Signal Propagation
Radio Bands and Bandwidth
Spread Spectrum Transmission
802.11 WLAN Operation
802.11 Transmission Standards
Wireless Mesh Networking

---
6.8 Frequency Spectrum, Service Band, Channels
6.8 Frequency Spectrum, Service Band, Channels
0 Hz

---
6.8 Frequency Spectrum, Service Band, Channels
6.8 Frequency Spectrum, Service Band, Channels

---
6.8 Frequency Spectrum, Service Band, Channels
6.8 Frequency Spectrum, Service Band, Channels

---
6.9 Signal Bandwidth
6.9 Signal Bandwidth

---
6.10: Channel Bandwidth and Transmission Speed
6.10: Channel Bandwidth and Transmission Speed
Channel Bandwidth
  - Channel bandwidth is the highest frequency in a channel minus the lowest frequency.
  - An 88.0 MHz to 88.2 MHz channel has a bandwidth of 0.2 MHz (200 kHz).
  - Higher-speed signals need wider channel bandwidths.

---
6.10 Channel Bandwidth and Transmission Speed
6.10 Channel Bandwidth and Transmission Speed
Transmission Speed and Channel Bandwidth
  - There is a direct relationship between required transmission speed and required channel bandwidth
  - Doubling bandwidth doubles the possible transmission speed
  - Multiplying bandwidth by N makes possible N times the transmission speed

---
6.10 Channel Bandwidth and Transmission Speed
6.10 Channel Bandwidth and Transmission Speed
Broadband Channels
  - Broadband means wide radio channel bandwidth and therefore high speed
  - Popularly, fast systems are called “broadband” even if they are not radio systems

---
6.11 2.4 GHz and 5 GHz Service Band
6.11 2.4 GHz and 5 GHz Service Band
The 2.4 GHz Service Band
  - 2.4 GHz to 2.485 GHz
  - Propagation characteristics are good
  - For 20 MHz 802.11 channels, only three nonoverlapping channels are possible
  - Channels 1, 6, and 11

---
6.11 2.4 GHz and 5 GHz Service Band
6.11 2.4 GHz and 5 GHz Service Band
The 2.4 GHz Service Band
  - Co-channel interference between nearby access points transmitting in the same channel degrades performance
  - Except in very small networks, difficult or impossible to put nearby access points on different channels (Figure 6-12)

---
6.11 2.4 GHz and 5 GHz Service Band
6.11 2.4 GHz and 5 GHz Service Band
The 5 GHz Service Band
  - More bandwidth, so between 11 and 24 non-overlapping 20 MHz channels
  - Makes it easy to have nearby access points operate on non-overlapping channels
  - Increasing channel bandwidth in newer standards reduces the number of possible channels

---
6.11 2.4 GHz and 5 GHz Service Band
6.11 2.4 GHz and 5 GHz Service Band
- What is the main advantage of 2.4 GHz operation?
- What is the main advantage of 5 GHz operation?

---
6.12 Co-Channel Interference, 2.4 GHz Band
6.12 Co-Channel Interference, 2.4 GHz Band
The 2.4 GHz Unlicensed Band
  - Difficult or impossible to put nearby access points on different channels

---
6.12 Co-Channel Interference, 2.4 GHz Band
6.12 Co-Channel Interference, 2.4 GHz Band

---
6.13 Licensed & Unlicensed Service Bands
6.13 Licensed & Unlicensed Service Bands
Licensed Radio Bands
  - If two nearby radio hosts transmit in the same channel, their signals will interfere
  - Most radio bands are licensed bands, in which hosts need a license to transmit: FM radio, etc.
  - The government limits licenses to control interference
  - In cellular telephone bands, only the central antennas are licensed, not the mobile phones

---
6.13 Licensed & Unlicensed Service Bands
6.13 Licensed & Unlicensed Service Bands
Unlicensed Radio Bands
  - A few service bands are set aside as unlicensed bands
  - Hosts in these service bands do not need to be licensed to be turned on or moved
  - Anybody can operate anywhere

---
6.13 Licensed & Unlicensed Service Bands
6.13 Licensed & Unlicensed Service Bands
Unlicensed Radio Bands
  - 802.11 Wi-Fi operates in unlicensed radio bands
  - This allows access points and hosts to be moved freely

---
6.13 Licensed & Unlicensed Service Bands
6.13 Licensed & Unlicensed Service Bands
Unlicensed Radio Bands
  - However, there is no legal recourse against interference from other nearby users
  - Your only recourse is to negotiate
  - At the same time, you may not cause unreasonable interference by transmitting at illegally high power

---
Introduction
Radio Signal Propagation
Radio Bands and Bandwidth
Spread Spectrum Transmission
802.11 WLAN Operation
802.11 Transmission Standards
Wireless Mesh Networking

---
Spread Spectrum Transmission
Spread Spectrum Transmission
Spread Spectrum Transmission
  - You are required by law to use spread spectrum transmission in the 2.4 and 5 GHz bands.
  - Spread spectrum transmission reduces propagation problems.
    - Especially multipath interference
  - Spread spectrum transmission is NOT used for security in WLANs.

---
6.14: Normal vs Spread Spectrum Transmission
6.14: Normal vs Spread Spectrum Transmission
Why do you not want to make radio channel bandwidth greater than the signal requires?

---
6.14: Normal vs Spread Spectrum Transmission
6.14: Normal vs Spread Spectrum Transmission
Wasteful of bandwidth but necessary
to avoid propagation problems.

---
6.15: Orthogonal Frequency Division Multiplexing
6.15: Orthogonal Frequency Division Multiplexing

---
Introduction
Radio Signal Propagation
Radio Bands and Bandwidth
Spread Spectrum Transmission
802.11 WLAN Operation
802.11 Transmission Standards
Wireless Mesh Networking

---
6.16 Typical 802.11 Wi-Fi Operation
6.16 Typical 802.11 Wi-Fi Operation
Sender puts a packet for the destination
host into an 802.11 frame, then sends the
frame wirelessly to the access point.

---
6.16 Typical 802.11 Wi-Fi Operation
6.16 Typical 802.11 Wi-Fi Operation
The 802.11 frame has the wrong frame format to travel over an 802.3 Ethernet network. The switches and destination host would not know what to do with it.
The access point removes the packet from the 802.11 frame and discards the frame.

---
6.16 Typical 802.11 Wi-Fi Operation
6.16 Typical 802.11 Wi-Fi Operation
The access point encapsulates the packet in an 802.3 frame and sends this frame on to the destination host via Ethernet switches.

---
6.16 Typical 802.11 Wi-Fi Operation
6.16 Typical 802.11 Wi-Fi Operation
The Wired Ethernet Network is called the Distribution System
The server removes the packet from the 802.3 frame.

---
6.16 Typical 802.11 Wi-Fi Operation
6.16 Typical 802.11 Wi-Fi Operation
- Does the IP packet travel all the way to the destination host?
- Does the 802.11 frame travel all the way to the destination host? Why or why not?

---
6-17: Basic Service Set (BSS)
6-17: Basic Service Set (BSS)
- An access point and its wireless hosts
- Service Set ID (SSID) is the name of the network (abc)

---
6-17: Extended Service Set (ESS)
6-17: Extended Service Set (ESS)
Collection of access points that all have the same SSID

---
6.18: Transmitting in a Single Channel
6.18: Transmitting in a Single Channel

---
6.18: Transmitting in a Single Channel
6.18: Transmitting in a Single Channel

---
6.19: CSMA/CA+ACK
6.19: CSMA/CA+ACK
Box
Carrier Sense Multiple Access with Collision Avoidance and Acknowledgement
  - Mandatory for 802.11 Wi-Fi Operation
- Carrier Sensing with Multiple Access
  - Sender listens for traffic (senses the carrier)
  - If another device is transmitting, it waits
  - This controls access by multiple devices that must not transmit simultaneously

---
6.19: CSMA/CA+ACK
6.19: CSMA/CA+ACK
Box
Collision Avoidance
  - When the current sender stops, two or more waiting devices may immediately want to transmit
  - This will cause a collision
  - Instead, the devices must wait a randomized amount of time before sending
  - This usually avoids collision, but it is inefficient

---
6.19: CSMA/CA+ACK
6.19: CSMA/CA+ACK
Box
ACK (Acknowledgement) and Reliability
  - Receiver immediately sends back an acknowledgement
  - CA random delay for other devices guarantees there will be enough time for an immediate ACK
  - If sender does not receive the acknowledgement, it retransmits using CSMA

---
6.19: CSMA/CA+ACK
6.19: CSMA/CA+ACK
Box
ACK (Acknowledgement) and Reliability
  - CSMA/CA plus ACK is a reliable protocol
  - Reliable protocols are rare in wired networks
  - However, radio transmission is unreliable enough to warrant it

---
6.20: CSMA/CA+ACK
6.20: CSMA/CA+ACK
Box
Inefficiency
  - There is a lot of waiting with CSMA/CA+ACK
  - This makes it inefficient

---
6.20: RTS-CTS
6.20: RTS-CTS
Box

---
6.20: RTS-CTS
6.20: RTS-CTS
Box

---
6.20: RTS-CTS
6.20: RTS-CTS
Box

---
6.20: RTS-CTS
6.20: RTS-CTS
Box
0

---
Comparison
Comparison
Box
CSMA/CA is Mandatory
  - It is the default MAC method.
  - It is more efficient than RTS/CTS.
- RTS/CTS
  - Is usually optional.
  - Is good if two or more client stations cannot hear each other.
  - Stop them from transmitting at the same time.

---
Introduction
Radio Signal Propagation
Radio Bands and Bandwidth
Spread Spectrum Transmission
802.11 WLAN Operation
802.11 Transmission Standards
Wireless Mesh Networking

---
6.21 Major 802.11 Wi-Fi Standards
6.21 Major 802.11 Wi-Fi Standards
Standard	Rated Speed
802.1g	54 Mbps
802.11a	54 Mbps
802.1n	100 to 600 Mbps 150 to 300 Mbps common
802.1ac	433 Mbps to 6.93 Gbps 433 to 1.3 Gbps common

---
6.21 Major 802.11 Wi-Fi Standards
6.21 Major 802.11 Wi-Fi Standards
Standard	Status
802.1g	Obsolescent but still used
802.11a	Obsolescent but still used
802.1n	Dominates the installed base today
802.1ac	Dominates sales today

---
6.21 Major 802.11 Wi-Fi Standards
6.21 Major 802.11 Wi-Fi Standards
Standard	Unlicensed Bands
802.1g	2.4 GHz
802.11a	5 GHz
802.1n	2.4 GHz and 5 GHz
802.1ac	5 GHz

---
6.21 Major 802.11 Wi-Fi Standards
6.21 Major 802.11 Wi-Fi Standards
Standard	Channel Bandwidth
802.1g	20 MHz
802.11a	20 MHz
802.1n	40 MHz but will drop back to 20 MHz if there is interference from a 802.1g or 802.1a channel
802.1ac	80 MHz and 160 MHz

---
6.21 Major 802.11 Wi-Fi Standards
6.21 Major 802.11 Wi-Fi Standards
Standard	Channels in 5 GHz Band in the USA
802.1g	NA (2.4 GHz only)
802.11a	20-25
802.1n	20-25 at 20 MHz / 8-12 at 40 MHz
802.1ac	4-6 at 80 MHz / 1-2 at 160 MHz
Wider channels means fewer channels

---
6.22: MIMO
6.22: MIMO
Access point transmits two signals in the same channel—one from Antenna A and
one from Antenna B.
These are called spatial streams.

---
6.22: MIMO
6.22: MIMO
The two signals arrive at different times at the two receiving antennas. Time differences allow them to be separated and understood.

---
6.22: MIMO (Multiple Input/Multiple Output)
6.22: MIMO (Multiple Input/Multiple Output)
MIMO Two Benefits
  - MIMO brings higher speeds because it can send more information in a channel.
  - MIMO also brings longer propagation distances for technical reasons we will not discuss.

---
6.23: Beam Forming
6.23: Beam Forming
Beamforming allows an access point to focus its transmissions and reception

---
6.23: Beam Forming
6.23: Beam Forming
Multiuser MIMO (MU-MIMO) allows two wireless hosts
to transmit at the same time.

---
Multiuser MIMO
Multiuser MIMO
- Defined in 802.11n, but a single method was not defined
- Defined in 802.11ac, and there is a single standard, so adoption is more likely
- However, initial pre-standard 802.11ac products typically do not offer it.

---
6.21 Major 802.11 Wi-Fi Standards
6.21 Major 802.11 Wi-Fi Standards
Standard	MIMO?	Maximum Spatial Streams	MU-MIMO?
802.1g	No	NA	No
802.11a	No	NA	No
802.1n	Yes	4	No
802.1ac	Yes	8	Yes

---
6.24 Speed, Distance, and Throughput
6.24 Speed, Distance, and Throughput
Rated Speed versus Throughput
  - Rated speed is the speed the standard specifies
  - Throughput is the speed that is actually delivered
  - Total throughput is substantially lower than rated speed—sometimes 50% lower

---
6.24 Speed, Distance, and Throughput
6.24 Speed, Distance, and Throughput
Aggregate versus Individual Throughput
  - Access point throughput is aggregate throughput for all devices transmitting and receiving
  - Its capacity is shared by all stations currently sending or receiving
  - Individual throughput can be much lower than aggregate throughput

---
6.24 Speed, Distance, and Throughput
6.24 Speed, Distance, and Throughput
Throughput versus Distance
  - As distance from the access point increases, signals get weaker
  - Wireless hosts must use slower but more reliable bit encoding methods—send fewer bits per clock cycle
  - This reduces individual throughput for these devices

---
6.25 Backward Compatibility
6.25 Backward Compatibility
Devices Built for Newer Standards Still Implement Older Standards
  - This is called backward compatibility
  - This Allows Older and Newer Devices to Communicate

---
6.25 Backward Compatibility
6.25 Backward Compatibility
Example of Backward Compatibility
  - Newer product: 802.11ac in the 5 GHz band
  - Older product: 802.11n in the 2.4 GHz band
  - The newer product will drop back to the standard the older product can use
  - They will communicate using the 802.11n standard in the 2.4 GHz band
  - They will only get 802.11n speeds

---
Introduction
Radio Signal Propagation
Radio Bands and Bandwidth
Spread Spectrum Transmission
802.11 WLAN Operation
802.11 Transmission Standards
Wireless Mesh Networking

---
6.26: Wireless Mesh Network
6.26: Wireless Mesh Network
There is no Ethernet network
(distribution system)
Frames are forwarded by access points
and wireless hosts

---
6.26: Wireless Mesh Network
6.26: Wireless Mesh Network
Mesh networks are governed by 802.11s
It is not a mature standard